## Slide 1: Traffic Signal Construction and Inspection in Pennsylvania
Chapter 3:
Plan Sheets and Other Contract Documents
Notes: Welcome to Module 3 of the Traffic Signal Construction and Inspection in Pennsylvania e-learning course. In this module, we will discuss traffic signal plan sheets and related contract documents.

## Slide 2: Traffic Signal Plans
Purpose of a Signal Plan
  Important document that illustrates the placement (proposed or existing) of the components required for a traffic signal installation
Manual Section 3.1

## Slide 3: Purpose of a Signal Plan
Purpose of a Signal Plan
  The plan is used for, but is not limited to, the following:
    The permit process (permit plan)
    Facilitating the contractor’s bid
    Building the signal (construction plan)
    Operating/maintaining the signal
    Signal locates
    Tort claims/lawsuits

## Slide 4: Traffic Signal Plan Items (1 of 2)
Traffic Signal Plan
  Plan Includes:
    Construction baseline
    Roadways, shoulders, curbs, curb ramps, sidewalks, islands, inlets, and all utilities
    Pavement markings
    Signal supports, controller, junction boxes, signal heads, detectors, pedestrian accommodations, and luminaires
    Movement, phasing, and sequence chart, including preemption and emergency flashing operation
    Electrical distribution
    Structure sizes, location, offsets, and orientation relative to the construction baseline
    Tabulation of quantities

## Slide 5: Traffic Signal Plan Items (2 of 2)
Traffic Signal Construction Plans
  Typical information found in a Traffic Signal Plan sheet includes the following
    Sign Tabulation
    Movement, Phasing and Sequence Chart
    Phasing Diagram
    Signal Identification
    Legend

## Slide 6: Traffic Signal Construction Plans (1 of 2)
Traffic Signal Construction Plans
  Typical information found in a Traffic Signal Plan sheet includes the following
    Sign Tabulation
    Movement, Phasing and Sequence Chart
    Phasing Diagram
    Signal Identification
    Legend

## Slide 7: Traffic Signal Construction Plans (2 of 2)
  List Continued:
    Title Block
    Notes
    Signal Wiring Diagram
    Upper Title Block
    Intersection Layout
    Traffic Signal Supports
    Electrical and Conduit Items
    Detectors
    Miscellaneous

## Slide 8: Parts of a Construction Plan
Parts of a Construction Plan

## Slide 9: Movement, Sequence and Timing Chart
Movement, Sequence and Timing Chart

## Slide 10: Emergency Pre-emption Phasing Chart
Emergency Pre-emption Phasing Chart

## Slide 11: Signals Legend
Signals Legend

## Slide 12: Wiring Diagram
Wiring Diagram

## Slide 13: Signature Block
Signature Block

## Slide 14: Legend
Legend

## Slide 15: Emergency Pre-Emption Notes
Emergency Pre-Emption Notes

## Slide 16: Coordination Plan
Coordination Plan

## Slide 17: Signing Table
Signing Table

## Slide 18: Special Provisions
Should be written in accordance with Publication 51, Chapter 1, Section E, Special Provisions
Only items that are not standard Publication 408 items need a special provision
Consult the local PennDOT engineering District and/or Central Office to confirm if a standard special provision exists for an item that may be needed under a traffic signal design project
Manual Section 3.2
Notes: Discuss what inspector does with the special provisions. Items not covered in pub 408.

## Slide 19: Municipal Traffic Signal Specifications
Consideration should be given to municipal traffic signal specifications during the design process
If a municipality has an adopted technical specification for traffic signal installations, the designer and project owner should do their best to accommodate the municipality’s needs since the municipality is the permittee and ultimate owner of the traffic signal
Manual Section 3.3
Notes: First bullet – that was taken into account during the design process. If the munic. Asks for something later, section in Pub 46. Section 408 has information too.

## Slide 20: Coordination of Plans and Specifications
In case of a discrepancy among the contract documents, the following order of precedence will apply:
  Special Provisions
  Plans (excluding cited Standard Drawings)
  Specifications (other than Special Provisions)
  Standard Drawings
Manual Section 3.4

## Slide 21: As-Built (Record) Plans
Once the signal installation has been accepted, as-built (record) drawings need to be made and sent in with the semi‐final records
Note for traffic signal projects are changes in:
  location of junction boxes
  vehicle signal heads
  conduit runs
  wiring
  pole locations
  utilities
Manual Section 3.5

## Slide 22: Module 3 Completion
You have now completed Module 3, Plan Sheets and Other Contract Documents
To review any section in this module, use the “Outline” on the left
Up next is Module 4, Materials and Products
It is suggested that you complete Module 4 before proceeding to the additional modules

## Slide 23: Remaining Modules
The remaining modules include:
  Module 4: Materials and Products
  Module 5: Traffic Signal Construction
  Module 6: Traffic Signal Inspection
Return to the PennDOT Technical Training Calendar to select Module 4